Int. No. 592

By Council Members Chin, Gentile, James, Koppell, Lander, Rose, Williams, Jackson, Arroyo, Levin and Ulrich

..Title

A Local Law to amend the New York city mechanical code, in relation to filtering soot from incoming air in buildings.

..Body

Be it enacted by the Council as follows:

Section 1. Section MC 605 of the New York city mechanical code, as added by local law number 33 for the year 2007, is amended by adding a new subsection 605.2.1 to read as follows:

605.2.1 Standards for air-handling units.  Air-handling units of mechanical ventilation systems, any portion of which provide outdoor air ventilation, shall be equipped with a particulate matter filtration system in accordance with ASHRAE 62.1 having a minimum efficiency reporting value (MERV) of 11 or greater in accordance with ASHRAE 52.2.

Exceptions:

1.	Subsection 605.2.1 shall not apply to the alteration or repair of a mechanical ventilation system that was installed prior to January 1, 2012 unless such alteration or repair includes the replacement or addition of an air-handling unit  in such system.

2.	Subsection 605.2.1 shall not apply to any  air-handling unit with a design capacity of less than 5,000 cfm.

§2.  The list of referenced standards of ASHRAE (American Society of Heating, Refrigerating and Air-Conditioning Engineers) as set forth in chapter 15 of the New York city mechanical code is amended by adding two new standards to read as follows:

| ASHRAE | American Society of Heating, Refrigerating and Air-Conditioning Engineers, Inc. 1791 Tullie Circle, NE Atlanta, GA 30329-2305 |
| --- | --- |
| Standard Reference Number | Title |
| 52.2 - 2007 62.1 - 2010 | Method of Testing General Ventilation Air-Cleaning Devices for Removal Efficiency by Particle Size Ventilation for Acceptable Indoor Air Quality |  |

§3. This local law shall take effect ninety days after its enactment, except that the commissioner of buildings shall take such actions as are necessary for its implementation, including the promulgation of rules, prior to such effective date.

JH/JTB

LS 2497

5-20-11