Int. No. 1093

By Council Members Levin, Chin, Comrie, James, Lander, Mendez, Richards, Rose and Gentile

..Title

A Local Law to amend the administrative code of the city of New York and the New York city building code, in relation to removing barriers to usage of temporary flood control and response devices.

..Body

Be it enacted by the Council as follows:

Section 1. Section 18-109 of the administrative code of the city of New York, as amended by chapter 100 of the laws of 1963 and recodified by chapter 907 of the laws of 1985, is amended by adding a new subdivision c to read as follows

c. This section shall not prevent or make unlawful the installation of temporary stairs or ramps complying with section BC 3202.4.3 of the New York city building code.

§2. Section 18-113 of the administrative code of the city of New York, as added by local law number 42 for the year 1939 and recodified by chapter 907 of the laws of 1985, is amended by adding a new subdivision c to read as follows:

c. This section shall not prevent or make unlawful the installation of temporary stairs or ramps complying with section BC 3202.4.3 of the New York city building code.

§3. Section BC 3202.1.1 of the New York city building code, as added by local law 33 for the year 2007, is amended to read as follows:

3202.1.1 Footings. Exterior wall and column footings may be constructed to project beyond the street line not more than 12 inches (305 mm), provided that the top of the footing is not less than 8 feet (2438 mm) below the ground or sidewalk level. Foundation walls required to support permitted projections may be constructed to project not more than the permitted projection beyond the street line. In areas of special flood hazard, continuous footings for the support and attachment of removable dryfloodproofing barriers or shields may be constructed to project beyond the street line not more than 12 inches (305 mm) both at grade and below grade.

§4. Section BC 3202.2 of the New York city building code, as added by local law 33 for the year 2007, is amended by adding a new subsection BC 3202.2.1.9 to read as follows:

3202.2.1.9 Footings for dryfloodproofing barriers or shields. In areas of special flood hazard, continuous footings for the support and attachment of removable dryfloodproofing barriers or shields may be constructed to project beyond the street line not more than 12 inches (305 mm) both at grade and below grade.

§5. Section BC 3202.4 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

3202.4 Temporary encroachments. Encroachments of temporary nature shall comply with Sections 3202.4.1 [and 3202.4.2] through 3202.4.3.

§6. Section BC 3202.4 of the New York city building code, as added by local law 33 for the year 2007, is amended by adding a new subsection BC 3202.4.3 to read as follows:

3202.4.3 Temporary stairs and ramps in areas of special flood hazard. In areas of special flood hazard, temporary stairs and ramps complying with Section G308.5 shall be permitted.

§7. Section BC G308 of the New York city building code, as added by local law 33 for the year 2007, is amended by adding a new section BC G308.5 to read as follows:

G308.5 Temporary stairs and ramps. Temporary stairs and ramps providing access to elevated doors or elevated means of egress as described by Item 3 of Section 6.2.2 of ASCE 24 shall comply with the applicable provisions of Chapters 10 and 11 of this code.

§8. Section 6.2.2 of Section BC G501.1 of the New York city building code, as added by local law number 33 for the year 2007, is amended to read as follows:

Section 6.2.2. [Item 3 of] Section 6.2.2 (Dry Floodproofing Requirements) is amended by modifying Item 3 and by adding a new exception to the end of section 6.2.2 to read as follows:

3. Have either:

3.1. All required means of egress elevated to or above the applicable [DFE] design flood elevation specified in Table 6-1, capable of providing human ingress and egress during the design flood; or

3.2. At least one elevated door located in close proximity to each required means of egress to the exterior that is to be blocked by flood shields or flood control devices, such that the face of the elevated door itself, and not merely its directional signage, is clearly visible to a person approaching the blocked egress door(s). Such door(s) shall be elevated to at or above the applicable [DFE] design flood elevation specified in Table 6-1, capable of providing human ingress and egress during the design flood. Such door(s) shall meet all New York City Building Code requirements for a required means of egress to the exterior of the structure including hardware and signage, but shall not be required to comply with the occupant load calculations, unless the structure is intended for occupancy during the design flood. Such door may be accessed by open steps and shall not be required to comply with Chapter 11 of the New York City Building Code if its only purpose is to provide the supplemental egress and ingress during conditions of flooding and to provide emergency egress at other times.

Exception: During a flood, nonresidential buildings that have been entirely evacuated, except for emergency personnel, shall not be required to maintain more than one means of egress complying with Item 3.

§9. Section BC G501.1 of the New York city building code , as added by local law 33 for the year 2007,is amended by adding a new subsection 6.2.3 to read as follows:

Section 6.2.3. Section 6.2.3 (Limits on Human Intervention) is amended to read as follows:

Section 6.2.3 Limits on Human Intervention. Dry floodproofing measures that require human intervention to activate or implement prior to or during a flood, including temporary stairs or ramps providing access to elevated doors or elevated means of egress, as described by Item 3 of Section 6.2.2, shall be permitted only when all of the following conditions are satisfied:

1. The flood warning time (alerting potential flood victims of pending flood situation) shall be a minimum of 12 hours, unless the community operates a flood warning system and implements an emergency plan to ensure safe evacuation of flood hazard areas, in which case human intervention is allowed only if the community can provide a minimum flood warning time equal to or longer than the cumulative

(a) time to notify person(s) responsible for installation of floodproofing measures, plus

(b) time for responsible persons to travel to structure to be floodproofed, plus

(c) time to install, activate, or implement floodproofing measures, plus

(d) time to evacuate all occupants from the flood hazard area;

2. All removable shields or covers for openings such as windows, doors, and other openings in walls and temporary stairs or ramps providing access to elevated doors or elevated means of egress as described by Item 3 of Section 6.2.2 shall be designed to resist flood loads specified in Section 1.6; and

3. Where removable shields or temporary stairs or ramps providing access to elevated doors or elevated means of egress as described by Item 3 of Section 6.2.2 are to be used, a flood emergency plan shall be approved by the authority having jurisdiction and shall specify, at a minimum, the following information: storage location(s) of the shields and temporary stairs and ramps; the method of installation; conditions activating installation; maintenance of shields and attachment devices and temporary stairs and ramps; periodic practice of installing shields and temporary stairs and ramps; testing sump pumps and other drainage measures; and inspecting necessary material and equipment to activate or implement floodproofing. The flood emergency plan shall be permanently posted in at least two conspicuous locations within the structure.

§10. This local law shall take effect immediately.

EAA

6/19/2013 3:54PM