Int. No. 796

By Council Members Lappin (in conjunction with the Mayor), Comrie, Gentile, Jackson, James, Koppell, Monserrate, Nelson, Palma, Recchia Jr., Seabrook, Stewart, Weprin and Gerson.

..Title

A Local Law to amend the administrative code of the city of New York, in relation to tower and climber cranes.

..Body

Be it enacted by the Council as follows:

Section 1.  Section 3302.1 of the building code of the city of New York is amended by adding the following definitions in alphabetical order:

CLIMBING.  The raising or lowering of a tower or climber crane to different floors or levels of a building or structure.

DISMANTLING.  The process of taking apart, piece by piece, in a specific sequence, the components of a crane.  Dismantling shall include climbing and jumping.

ERECTION.  The assembly and placement of crane sections and components into place, including all operations incidental thereto.  Erection shall include climbing and jumping.

§2.  The building code of the city of New York is amended to add a new section 3319.8 to read as follows:

3319.8 Special provisions for tower and climber cranes.  Tower and climber cranes shall comply with the following requirements:

3319.8.1 Plan for the erection, jumping, climbing, and dismantling of tower or climber cranes.  An erection, jumping, climbing and dismantling plan for tower or climber cranes, other than truck and crawler mounted tower cranes, shall be submitted to the department by a licensed engineer.  The plan must be prepared by a licensed engineer in conjunction with a licensed rigger and must be in compliance with the manufacturer’s recommendation for erection, jumping, climbing, or dismantling of the specific crane where such manufacturer’s recommendations exist.  The plan must be filed with the certificate of on-site inspection application as required by section 3319.3.  No erection, jumping, climbing, or dismantling of a tower or climber crane shall take place without the prior issuance of a certificate of on-site inspection by the cranes and derricks unit.  The plan shall include the following:

- Identification of the equipment proposed to be used; including all machines proposed to be used in the erection or dismantling;

- A detailed identification of the assemblies and sub-assemblies required for the erection and dismantling of the equipment;

- Location of the equipment, sidewalk sheds (or Department of Transportation street closing permits, if applicable), surrounding buildings, protection for their roofs and the pick-up points, loads, and radius of swing of all loads. In addition, the safe load from the approved load radius chart shall be submitted for lift radius;

- A weight list of all assemblies and sub-assemblies proposed to be lifted. Components are to be clearly marked with their weight painted on the assembly or stamped on metal tags attached to the assembly.  The manufacturer of the climber or tower crane shall certify the weight of assemblies and sub-assemblies. Alternately, the licensed engineer applicant shall certify an erection, jumping, climbing or dismantling weight list indicating how such weights were determined;

- The center of gravity of all asymmetrical components shall be located and shown;

- A sequence of operation detailing the erection, jumping, climbing, and dismantling, along with the rigging materials to be used in such operations;

- The certification of the calibration as required in item 6 of section 3319.8.8;

- Cranes or derricks located either within the lot line or on the street and used to erect, jump, climb, or dismantle a tower or climber crane shall be indicated;

- A time schedule including date and time of day that the erection, jumping, climbing, or dismantling is proposed to take place. Erection, jumping, climbing, or dismantling shall not be conducted prior to sunrise, or after sunset; and

- The names and contact information of the licensed climber or tower crane rigger, and the crane safety coordinator or designee, along with the name and contact information of the company performing the erection, dismantling, climbing and/or jumping work.

3319.8.2 Safety coordination meeting.  The general contractor must hold a safety coordination meeting prior to the initial jump or climb, as well as the dismantling or initial jump down, of a climber or tower crane.  No work related to the erection, climbing, jumping or dismantling of the tower or climber crane may be performed without the safety coordination meeting having taken place.  The following parties must be present at the safety coordination meeting:

- General contractor or designee;

- Professional engineer of record for the crane or designee;

- Licensed tower or climber crane rigger;

- Crane safety coordinator;

- Site safety manager or coordinator, if required for the job by Chapter 33 of the code; and

- Any other parties the department deems necessary.

3319.8.3 Pre-jump safety meeting.  The general contractor must coordinate a pre-jump safety meeting no more than 24 hours prior to each instance of a tower or climber crane jump or climb.  No work related to the jumping or climbing of the tower or climber crane may be performed without the pre-jump safety meeting having taken place. The following parties must be present at the pre-jump safety meeting:

- General contractor or designee;

- Licensed tower or climber crane rigger;

- Crane safety coordinator;

- Site safety manager or coordinator, if required for the job by Chapter 33 of the building code;

- Crane operator and oiler;

- “Jumping” crew and back-up personnel;

- Flagman/woman;

- Signalman/woman and communications personnel; and

- Any other parties the department deems necessary.

3319.8.4 Department notification of meetings.  The general contractor must notify the department at least 48 hours in advance of any safety coordination meeting or pre-jump safety meeting.  No work related to the erecting, jumping, climbing, or dismantling of the tower or climber crane is to be performed without prior notice of the meeting having been given to the department.

3319.8.5 Safety coordination and pre-jump safety meeting topics.  The following topics are to be covered during safety coordination and pre-jump safety meetings:

- Scope of work;

- Roles and responsibilities;

- Rigging to be used and the specific sequence of operations;

- Inspection of all rigging equipment, materials, and tools prior to work;

- Review of all equipment, including but not limited to, collars, ties, and bolts;

- Permit validity;

- Qualifications and training of personnel;

- Relevant weather warnings;

- Compliance with the manufacturer’s manual; and

- Softening mechanisms, if using nylon slings.

3319.8.6 Meeting log.  The general contractor, or his or her designee, and/or the company erecting, jumping, climbing, or dismantling the tower or climber crane shall keep a log on site and available to the department at all times that shall include:

  - the dates and times of all safety coordination meetings and pre-jump safety meetings held;

  - the names, titles, and company affiliations of all those present at the meetings;

  - a summary of what was discussed during each meeting, including specific tasks and the name of the person to whom they were assigned;

  - a list of the decisions made at the meeting; and

  - certification of worker training pursuant to Section 3319.8.2.

3319.8.7 Inspection and certification by the engineer of record.  Prior to jumping or climbing a tower or climber crane, the engineer of record for the crane must provide the department with a certified, signed, and sealed report stating that:

1.  he or she (or his or her designee) has inspected the crane installation prior to the pre-jump safety meeting, and providing the date of inspection;

2.  the crane is installed according to the plans approved by the department as well as in accordance with the manufacturer’s specifications;

3.  the engineer of record for the crane has reviewed and confirmed that the appropriate technical testing records for the crane, including torque, plumb, and magnetic particle reports, comply with all safety requirements and with the manufacturer’s specifications; and

4. he or she has found no hazardous conditions during the crane inspection or any other condition that might adversely affect the safety of erection, dismantling, climbing, or jumping operations.

3319.8.8 Erection, jumping, climbing, and dismantling operations.  The erection, jumping, climbing, and dismantling operations for tower and climber cranes shall be subject to the following requirements:

- The licensed tower or climber crane rigger, and the crane safety coordinator or designee, shall be present at the job site during erection, jumping, climbing, and dismantling of the tower or climber crane;

- Cranes or derricks located either within the lot line or on the street, and used to erect, jump, climb, or dismantle tower or climber cranes, shall be subject to certificate of on-site inspection requirements;

- A load radius chart approved by department shall be posted in the cabin of the crane;

- The approved erection, jumping, climbing, or dismantling procedure and sequence, with weights of assemblies and sub-assemblies clearly marked, shall be given to the operator of the crane or derrick and to the rigger prior to commencement of the work;

- No tower or climber crane shall be erected, jumped, climbed, operated, or disassembled in or over any roadway, sidewalk, or street unless a permit is first obtained from the New York City Department of Transportation;

- All accepted or approved installed safety devices on a crane involved in the erection, jumping, climbing, or dismantling procedure shall have been calibrated within the preceding three (3) months; and

- The safety devices of the tower or climber crane shall be inspected by the operator as part of the inspection procedure.

§3.  This local law shall take effect _____ days from its enactment.