Int. No. 935

By Council Members Gennaro, Comrie, Fidler, James, Koppell, Nelson, Weprin, Gerson and White Jr.

..Title

A Local Law to amend the administrative code of the city of New York, in relation to backflow prevention device reporting and certification.

..Body

Be it enacted by the Council as follows:

Section 1.  Legislative findings and intent.   The Council finds that plumbing cross-connections, points in the plumbing system where it is possible for used water, industrial fluids, gas or substances other than the intended potable water, to come into contact with the potable drinking water supply, are a significant public health risk.  Backflow of non-potable water or other substances from cross connections may take place when water flows in the opposite direction than that intended because a potable system is connected to a nonpotable supply under higher pressure than the distribution system as a result of a pump, boiler or elevation difference.  Backsiphonage of nonpotable water from cross connections may take place when negative pressure in a portion of the distribution system is below ambient pressure in the distribution system as a result of water main breaks, firefighting efforts or any high demand situation.

According to the United States Environmental Protection Agency (EPA), plumbing is often installed by persons who are “unaware of the inherent dangers of cross connections”.  Backflow and backsiphonage into the public water distribution system can be prevented by not creating cross-connections, by eliminating existing cross connections, by educating the public to prevent cross-connections and by correcting cross-connections that are found with installation of proper backflow devices or assemblies.    However because new cross-connections are routinely created, it is also useful to create impediments to backflow or back siphonage by installation of backflow prevention devices and assemblies.  The Council further finds that currently a plumber is under no duty to report a cross-connection should one be discovered and no procedure exists that requires annual filing of proof that an approved backflow prevention device was installed by any owner or operator of a facility that uses hazardous materials or that is legally required to install such a device, although both measures would help to reduce the potential adverse impacts from cross connections.

§2. Chapter 3 of title 24 of the administrative code of the city of New York is amended by adding a new section 24-343.1 to read as follows:

§24-343.1. Backflow prevention device reporting. (a) For purposes of this section the following terms shall have the following meanings:

(1) “Backflow and backsiphonage” shall mean the reversal of the normal direction of flow in a system caused by a negative pressure (vacuum or partial vacuum) in the supply piping.

(2) “Backflow prevention device” shall mean an approved air gap, reduced pressure zone device or double check valve assembly used to contain potential contamination within a facility.

(3) “Cross connection” shall mean a physical connection or arrangement between two separate piping systems where one system contains potable water and the other contains steam, gas, a chemical, or nonpotable water, and there may be a flow from one system to the other.

(4) “Hazardous facility” shall mean a facility in which substances may be present that may endanger the health of other water users if introduced into the public water system, including but not limited to, laboratories, sewage treatment plants, chemical plants, hospitals and mortuaries.

(5) “High hazardous facility” shall mean a buildings or space classified in the high hazard occupancy group when they are used for storing, manufacturing, or processing potentially-explosive products or materials, or highly-combustible or highly-flammable products or materials that are likely to burn with extreme rapidity. The high hazard group shall include, but not be limited to, uses that involve storing, processing, or handling any materials that produce explosive dust, or that result in the division of matter into fine particles subject to spontaneous ignition; uses that employ solids or substances that ignite or produce flammable gases on contact with water; and any other uses that constitute a high fire hazard because of the form, character, or volume of the materials involved.

(6) “Licensed master plumber” shall mean an individual authorized under the provisions of this subchapter to install, maintain, repair, modify, extend or alter plumbing, standpipe where a sprinkler is not or is not now being connected, domestic water, connections to the domestic water, combination domestic water and reserve standpipe supply tank, up to and including the roof tank check valve, gas piping or any piping system referred to in subchapter sixteen of chapter one of title twenty-seven of the code and in reference standard RS-16 and up to thirty sprinkler heads off the domestic water in any one building in the city of New York which has satisfied the provisions of this subchapter for operation pursuant to a plate, certificate issued to an individual and seal, and any partnership, corporation or other business association operating under the auspices of such individual.

(7) “Licensed plumber” shall mean anyone holding a plumbing license issued by the city of New York.

b. Whenever a licensed plumber or a licensed master plumber discovers or identifies a cross connection in a building or structure, prior to undertaking plumbing work, such licensed plumber or licensed master plumber shall be under a duty to immediately report the existence of the cross connection to the department and the property owner or if discovered during the course of emergency work, report the existence of a cross connection  as soon as possible after completion of such work.

c.  When the department or the owner or operator of a building or structure has determined that there is backflow or backsiphonage of hazardous materials from such building or structure into a city water main, private water main, or to an internal water main may occur, the owner or operator of such building or structure shall be under a duty to correct such backflow or backsiphonage and certify to the department that a backflow prevention device has been installed and where appropriate, that a backflow device has been replaced.  Where removal of a cross-connection or installation or replacement of a backflow device has been performed as part of a project for which a licensed professional engineer or registered architect has submitted plans, such licensed professional engineer or registered architect shall inspect and submit to the department a certification that the cross-connection has been removed or a backflow prevention device installed or replaced in conformity with the plans approved by the department or the department of buildings.

d. 1. On or before August 1, 2009, the department shall submit a report to the council setting forth the number of hazardous facilities, high hazard facilities and all other facilities which the department believes have had required backflow prevention devices installed and the number of facilities in each category that the department believes still require the installation of one or more backflow prevention devices. Every February first and August first thereafter, the department shall submit a report to the council containing the number of facilities in each category for which one or more backflow prevention devices were installed since the last report was required, the number of facilities in each category that the department has newly determined require the installation of such devices, and the number of violations issued for the failure to install a required backflow prevention device.

§4. This local law shall take effect ninety days after enactment.

LS #5789

SS  2/16/09