Int. No. 266

By Council Members Garodnick, Barron, Brewer, Gonzalez, James, Lander, Palma, Vann, Williams, Mark-Viverito, Lappin, Van Bramer, Recchia, Chin, Weprin, Gennaro and Jackson

..Title

A Local Law to amend the administrative code of the city of New York, in relation to energy efficiency in commercial buildings.

..Body

Be it enacted by the Council as follows:

Section 1. Section 28-1001.2 of the administrative code of the city of new York is amended to read as follows:

Add at the end of chapter five

Chapter 5 - Commercial Energy Efficiency

501.1 Add the following phrase between the words “Residential Buildings” and “or the requirements”: , as modified for New York City by Appendix A of this code

505.2.2.2 After the Exception, add a new paragraph to read as follows:

In addition to the above requirements, for the following spaces, an occupant sensor shall be installed that turns lighting on by manual control, and such occupant sensor shall not have an override switch that converts from manual-on to automatic-on functionality; however, the occupant sensor may have a grace period of up to 30 seconds to turn on the lighting automatically after the sensor has turned off the lighting if occupancy is detected:

1.	classrooms (not including shop classrooms, laboratory classrooms, and preschool classrooms),

2. 	conference/meeting rooms,

3. 	employee lunch and break rooms, and

4. 	offices smaller than 200 square feet.

Add at the end of chapter six

Chapter 6 - Referenced Standards

Add at end of the first paragraph the following:

Refer to the rules of the department for any subsequent modifications that may have been made to the referenced national standards set forth herein in accordance with the exception contained in Section 28-103.19 of the Administrative Code.  The application of the referenced standards shall be as specified in Section 102.8.

Add to section titled, “ASHRAE,” after the row heading “90.1-2007” an asterisk.

Add at end of section titled, “ASHRAE” a footnote to read as follows: * as modified in Appendix A

Appendix A - Modified Energy Standard

Add a new Appendix A after chapter 6 and before the Index to read as follows:

APPENDIX A

MODIFIED ENERGY STANDARD FOR BUILDINGS, EXCEPT FOR LOW-RISE RESIDENTIAL BUIDLINGS

SECTION ECC A101

SCOPE

A101.1 Scope. This appendix provides the modifications to the nationally recognized standard ASHRAE/IESNA Standard 90.1 Energy Standard for Buildings Except for Low-Rise Residential Buildings, governing commercial energy efficiency. Where a referenced publication has been modified for the City of New York as by the New York City Construction Codes and the New York City Energy Conservation Code, every reference to such publication shall be deemed to include all such modifications.

SECTION ECC A102

ENERGY STANDARD FOR COMMERCIAL BUILDINGS

A102.1 General. The standards for energy efficiency in commercial buildings as defined in Section 202 of this code shall be in accordance with Chapter 5 of this code or in accordance with ASHRAE/IESNA Standard 90.1 Energy Standard for Buildings Except for Low-Rise Residential Buildings, 2007 edition, modified for New York City as follows. Refer to the rules of the department for any subsequent additions, modifications or deletions that may have been made to this standard in accordance with Section 28-103.19 of the Administrative Code.

Add to the end of chapter 9

Chapter 9 - Lighting

9.4.1.2  Delete paragraph (a) of Section 9.4.1.2 and replace with the following:

a. 	An occupant sensor shall be installed that turns lighting on by manual control and automatically turns lighting off within 30 minutes of all occupants leaving a space or by manual control in the following spaces:

1.	classrooms (not including shop classrooms, laboratory classrooms, and preschool classrooms),

2. 	conference/meeting rooms,

3. 	employee lunch and break rooms, and

4. 	offices less than 200 square feet (18.5 m2) in area.

Such occupant sensor shall not have an override switch that converts from manual-on to automatic-on functionality, and the occupant sensor may have a grace period of up to 30 seconds to turn on the lighting automatically after the sensor has turned off the lighting if occupancy is detected.

Exception: offices less than 200 square feet (18.5 m2) in area equipped with lighting controls activated by photosensor.

§2. this local law shall take effect on January 1, 2011, except that the commissioner of buildings shall take such actions as are necessary for its implementation, including the promulgation of rules, prior to such effective date.

JH

6-4-10

EE 13

LS # 1003