Int. No. 1098

By Council Members Richards, Chin, James, Koo, Koppell, Lander, Mendez and Rose

..Title

A Local Law to amend the New York city plumbing code, in relation to preventing the backflow of sewage.

..Body

Be it enacted by the Council as follows:

Section 1. Section 715.1 of the plumbing code of the city of New York is amended by adding a new section 715.1.1 to read as follows:

715.1.1 Backwater valves in special flood hazard areas. Building drains serving buildings located in Special Flood Hazard Areas, as established by Section G102.2 of Appendix G of the New York City Building Code, shall be provided with a backwater valve at the point of exit from the building and downstream from the building trap.

§ 2. Section 1002.6 of the plumbing code of the city of New York is amended by adding a new section 1002.6.1 to read as follows:

1002.6.1 Backwater valves in special flood hazard areas. Backwater valves shall be provided on the building storm drainage system in accordance with Section 715 for all buildings located in the Special Flood Hazard Areas, as established by Section G102.2 of Appendix G of the New York City Building Code.

§ 3. This local law shall take effect ninety days after its enactment.

LS #

SS

6/13/13 11:03 a.m.