Int. No. 993

By Council Member Dilan, the Speaker (Council Member Quinn), and Council Members Fidler, Gonzalez, James, Liu, Nelson, Seabrook, Stewart, Weprin, Baez and White (in conjunction with the Mayor)

..Title

A Local Law to amend the administrative code of the city of New York, in relation to submittal documents for demolition.

..Body

Be it enacted by the Council as follows:

Section 1.  Section 3306.5 of the building code of the city of New York, as added by local law number 33 for the year 2007, is REPEALED and a new section 3306.5 is added to read as follows:

3306.5  Submittal documents for demolition.  Submittal documents for full and partial demolition shall comply with Sections 3306.5.1 and 3306.5.2.

3306.5.1 Required documents. Submittal documents shall be approved by the department before demolition work begins. Such submittal documents shall be signed, sealed, and submitted by a registered design professional and shall contain, at a minimum, the following:

1. Plans, sections, and details of the building or portion thereof to be demolished clearly showing the extent, sequence, and means and methods of demolition.

2. Bracing and shoring necessary to support all demolition operations through all sequences of the demolition.

3. Where mechanical demolition equipment, other than hand held devices, is to be used, a listing and description of all such proposed equipment to be used in the demolition, including the scope of equipment work and positioning of equipment on the existing structure. The description of the equipment shall include calculations showing adequacy of the existing structure to support loads imposed by such equipment. If more than one piece of demolition equipment is proposed to be used at the same time, the effect of the simultaneous loads imposed on the existing structure shall be described and investigated.

4. Description of compliance with the applicable provisions of Section 3306.9.

Exceptions:

1. Full demolition without the use of mechanical demolition equipment. The submittal documents listed in  Section 3306.5.1 are not required for full demolition where the demolition is to be accomplished without any mechanical demolition equipment, including handheld for:

1.1 One-, two- or three-family dwellings that are three stories or less; or

1.2. Buildings that are three stories or less and with a floor area of 5,000 square feet or less per story.

2. Full or partial demolition using mechanical demolition equipment.  The submittal documents required by Section 3306.5 for the full or partial demolition using mechanical equipment other than handheld shall be filed by an engineer.

3306.5.2 Maintenance of submittal documents.  The approved set of submittal documents shall be kept at the site at all times and be accessible for inspection.  It shall be a violation of this code to use mechanical equipment, whether handheld or other than handheld, to perform full or partial demolitions unless the approved submittal documents required by Section 3306.5.1 are available for inspection.  Failure to make submittal documents available on site may result in the issuance of a stop work order.

§2.  Section BC 3306 is amended by adding a new section 3306.11 to read as follows:

3306.11 Filing requirements.  Where submittal documents are required in connection with full or partial demolition in accordance with Section 3306.5, applications shall be filed  by the  registered design professional in accordance with Article 104 of Title 28.

§3. This local law shall take effect 90 days after its enactment into law.

RCC

BKH

05/07/09

7:30 p.m.

LS # 7083