Staff:	Terzah N. Nasser

Counsel

Barbara Turkewitz

Senior Policy Analyst

T H E   C O U N C I L

REPORT OF THE INFRASTRUCTURE DIVISION

KATHLEEN CUDAHY, DIRECTOR

COMMITTEE ON HOUSING AND BUILDINGS

Archie Spigner, Chair

June 27, 2000

PROPOSED INT. NO. 720-A:			By:	Council Member Spigner also Council Member O’Donovan

ADMINISTRATIVE CODE:			Amends subdivision b of section P102.2 of reference standard RS 16 of title 27.

TITLE:						In relation to the exterior use of plastic pipes and fittings for underground yard drainage and storm water piping.

BACKGROUND AND ANALYSIS:

New York City has been extremely cautious about the use of plastic piping in construction.  Currently plastic piping can only be used in residential buildings of three stories or less in height.  Throughout the country, plastic pipes have been used increasingly because they are a cost efficient alternative to traditional piping materials.  Int. No. 720-A expands the conditions for which plastic pipes can be used to permit the use of plastic piping, with a diameter of twelve inches or more, when used underground to carry yard drainage or when used to carry storm water.  Thus, under this legislation, plastic piping could be used outside of a building’s foundation during new construction or for the replacement of existing metal or concrete piping used to discharge to the sewer system.  This piping cannot be connected to any piping system linking to the inside of the building.

Amendments to Int. 720

Int. No. 720 was amended by eliminating the reference to the older commercial standards used for plastic pipe and fitting requirements in the interior of a residential building three stories or less, and by imposing the use of the newer American Society for Testing and Materials (ASTM) standards in this provision of the Reference Standards.  In addition, the International Association of Plumbing and Mechanical Officials (IAPMO) Installation Standards were updated to conform the standards to those acceptable by the Department of Buildings (DOB).  All standards updated in this provision are in conformity with those acceptable to DOB.